## Slide 1
Pointers for putting things in payload boxes
Plan (in 3D) in advance, possibly with “mock boxes”
  Be able to reach switches, change out batteries, extract SD cards, etc.
Nothing sticks well to Styrofoam
  Velcro/tape for temporary mounting
  Zip ties (external/military grade) for final mounting
    Daisy-chain as need be, pull tight then clip off loose ends
    Don’t cover camera views
    “Drill” holes rather than poking them to avoid spalling
Use lights to able to tell if things are working (even after the box is sealed, if possible)
Be willing to roll box down a flight of steps (but if steps might suffer, box might be “too tough”
Add chemical hand warmers for thermal inertia, especially to batteries
Make boxes black for a thermal boost but…
  …don’t let payloads overheat on the ground prior to launch – keep them in the shade!
Don’t forget a siren, with an external switch
Use fresh lithium batteries whenever possible, for better thermal performance
Avoid “windows” in front of cameras – they get fogged up
Check camera view in advance
Full clear memory cards prior to flight (i.e. delete, then empty trash)
Tether components, especially any mounted on the outside, as backup for zip ties

## Slide 2
Pointers for building and rigging custom payload boxes
Cut sides (or “order” them) based on plan
  Build box to accommodate the contents
Build with stapping tape
  avoid hot glue and epoxy –they get brittle
Don’t count on tape or Velcro sticking well to Styrofoam
  Always tape around until you reach tape (but one layer of strapping tape will suffice)
Plan which side (or top) will be openable to turn things on just prior to flight
  Seal quickly with ~2 wraps of strapping tape on the flight line
    Don’t cover camera views
  “Hinges” are optional, but can help lids from going missing
Add identification to outside and inside of every box
Add classic rigging line to 4 widely-separated corners of every box
  Rigging goes through tough tubing (NOT straws)
  Loops and key rings below box (exactly the same length)
  Triple knot above each tube so lines won’t slide up or down
  Loops at top of lines (exactly the same length) – to attach to key rings on box above
Can add rigging after box innards are complete done
Can make box black (with duct tape) after rigging is completely done
Test rigging with a “yank test”