## Slide 1: Introduction Arduino
Ballooning Bundle

## Slide 2: What is a Microcontroller?
Small computer with a processor core, memory and programmable input/output
Continuously repeats software commands
Example: Arduino

## Slide 3: Arduino UNO
USB Connector
Battery Connector
Power Pins
Analog Pins
Digital Pins

## Slide 4: Arduino MEGA
USB Connector
Battery Connector
Power Pins
Analog Pins
Digital Pins
Serial Pins

## Slide 5: Introduction to Software
Arduino has its own software development tool
  Can be downloaded for free
Comparable to C language
All programs must have setup and loop functions
Many things have off the shelf software prewritten
  Look online for example code and tutorials

## Slide 6: BareMinimum
void setup() {
// put your setup code here, to run once:
}
void loop() {
// put your main code here, to run repeatedly:
}

## Slide 7: Serial Communication
Transmit and Receive (TX and RX pins)
Arduino – Computer
GPS – Aduino

## Slide 8: Specialized Pins: SPI
Serial Peripheral Interface
Is a synchronous serial data protocol
Used by microSD shield, and MicroMagnetometer

## Slide 9: Specialized Pins: I2C Bus
Inter-Integrated Circuit
Uses two pins for communication
  SDA: Serial Data Line
  SCL: Serial Clock Line
On an Uno, pins A4 and A5 are used for I2C
Used by real time clock

## Slide 10: 1-Wire Digital Bus
Similar to I2C, only 1 digital pin used (1 wire)
Can support multiple sensors
Wire must be powered using 5V and a pull-up resistor to work
Used by digital temperature sensor